## Slide 1
Part I: Monday, 3 June @11:00
tactile sensing in nature
What is tactile sensing?
How is it used?
  in humans? in animals?
What exactly is being measured?
What insights can we draw for robotic tactile sensing in medical and related applications?
Mark R. Cutkosky
Stanford University 3 June 2013
Part II: Thursday, 6 June @14:00
basic issues, mechanics and trade-offs in tactile sensing
Part III: Monday, 10 June @11:00
implementations and applications
Notes: My name is Santhi Elayaperumal, I am speaking on MRI-Compatible Haptics…using strain sensing to predict 3-dimensional needle bending in real-time.

## Slide 2: Human mechanoreceptors
Cutkosky M.R. and Ulmen, J., “Dynamic tactile sensing,” in The Human Hand: A Source of Inspiration for Robotic Hands, R. Balasubrmanian and V. Santos, eds., Springer Verlag (in press).
Receptor | receptive field | frequency range | sensed quantity
FA-I Meissner corpuscles 140/cm^2 1cmcm^2cmfingertips | 3-4mm | 5-60 Hz | dynamic skin deformation
SA-I Merkel endings 70/cm^2 | 3-4mm | 0-5 Hz | compressive stresses
FA-II Pacini corpuscles | >20mm | 50-500+ Hz (peak sensitivity ~250 Hz) | vibration
SA-II Ruffini endings | >10mm | 0-10 Hz | directional skin stretch
table data from various sources (see Johansson & Flanagan 2009 for review)

## Slide 3
Start with some
hands-on
exercises
Cortical homunculus
Wilder Penfield ~1950
Notes: My name is Santhi Elayaperumal, I am speaking on MRI-Compatible Haptics…using strain sensing to predict 3-dimensional needle bending in real-time.

## Slide 4: Mapping mechanoreceptors
Johansson, R.S. and Flanagan, J.R.,
Coding and use of tactile signals
from the fingertips in object
manipulation tasks, Nature Reviews,
Vol. 10, May 2009, 345-357

## Slide 5: Thermal sensing
separate warm and cold receptors whose firing rate depends on magnitude of difference w.r.t body temperature
both slowly adapting (SA) and rapidly adapting (FA) characteristics, so depends on both T and dT/dt
perception strongly affected by body temperature versus temperature at surface of skin (aluminum feels cooler at room temperature than wood) -- an important component of material identification
R.K. Adair. A model of the detection of warmth and cold by cutaneous sensors through effects on voltage-gated membrane channels, PNAS 1999 96 (21).
free nerve endings
for temperature, pain

## Slide 6: Resolution
~ 17,000 mechanoreceptors in human hand
  (>100,000 in star nosed mole, 6 along body in C. elegans respond to 10μN force)
Spacing of afferents at fingertips to 140/cm2 for FA-I; 0.7mm mean spacing; receptive fields ~ 11mm2.
Resolution: two-point discrimination = 1-2 mm
Gratings with spacings to approximately 1mm (finer spacing = “texture”)
Discrete bumps on smooth surfaces down to a few microns (e.g. checking imperfections in paint)
Nonlinear neural response: where R = response, S = stimulus magnitude, b ~ 0.7, which increases dynamic range.
  However, subjects often report almost linear perception to varying stimuli.

## Slide 7: Tactile events in manipulation tasks
fingers
contact
object
object makes
or breaks
contact with
surface
contact
released
Johansson, R.S. and Flanagan, J.R., Coding and use of tactile signals
from the fingertips in object manipulation tasks, Nature Reviews,
Vol. 10, May 2009, 345-357

## Slide 8: Timing and coincidence
curved
flat
Although nerve conduction is slow and spike frequency is moderate
(~100/sec maximum), timing of first spikes can be interpreted
at peripheral nerves to give cues about loading sequence.
Johansson, R.S. and Flanagan, J.R., Coding and use of tactile signals
from the fingertips in object manipulation tasks, Nature Reviews,
Vol. 10, May 2009, 345-357

## Slide 9: Grasp force regulation is based on slips and incipient slips
B. Edin, R.D. Howe, G. Westling and M.R. Cutkosky, "Relaying Frictional Information to a Human Operator by Physiological Mechanisms," IEEE Transactions on Systems, Man, and Cybernetics, Vol. 23, No. 2, March/April 1993, pp. 427-432.
spontaneous slip: adjustment in ~80 ms
artificially induced slips - subjects did not habituate

## Slide 10: Pacinian corpuscle (FA-II) sensitivity to vibrations and Meissner (FA-I) sensitivity to small features
Adapted from data in Verrillo, R.T., Vibrotactile thresholds measured at the finger, Perception & Psychophysics, Vol. 9 (4) (1971).
Peak sensitivity
around 300 Hz.
Able to detect
bumps of a few
microns under
ideal conditions

## Slide 11: Haptic exploration and integration
Interview with blind field paleontologist Professor G.J. Vermeij, U.C. Davis Geophysics Dept.
http://www-cdr.stanford.edu/dml/previous_projects/vermeij/vermeij.html
Cutkosky & Costa 1995
Topics
Scales of space and time for exploration
Object recognition
Effects of cold
Exploratory procedures
Integration of information
http://www-cdr.stanford.edu/dml/previous_projects/vermeij/vermeij.html#seperate

## Slide 12: EPs: Exploratory Procedures
Lederman, S. and Klatzky, B.
Extracting object properties through
haptic exploration,
Acta Psychologica 84 (1993)
29-40.

## Slide 13: Anuran (frog) tactile responses
Tactile sensing triggers stereotypical responses [1-3]
Some evidence of primitive goals or “funnels” [4]:
Make any kind of contact, as soon as possible
Use both hands to pull on any graspable features
Bring object toward center of the manipulable workspace
Bring toward mouth
If something doesn’t work at first…
Keep trying!
Frogs grasping crickets (15 FPS) - A. Asbeck
[1] Gray, L.A. et al., Evolution of Forelimb Forelimb Movement Patterns for Prey Manipulation in Anurans, J. Exp. Zoology, 277:417–424 (1997)
[2] Comer, C. and Grobstein, P., Tactually Elicited Prey Acquisition Behavior in the Frog, Rana pipiens, and Comparison with Visually Elicited Behavior J Comp Physiol (1981) 142:141-150
[3] Ivanco, T.L. et al., Skilled forelimb movements in prey catching and in reaching by rats and opossums, Behavioural Brain Research, 79 (1996) 163-181
[4] Rizzi, A. et al., Sequential Composition of Dynamically Dexterous Robot Behaviors, IJRR 1999; 18; 534.

## Slide 14: Anuran (frog) tactile responses
Tactile sensing triggers stereotypical responses [1-3]
Some evidence of primitive goals or “funnels” [4]:
Make any kind of contact, as soon as possible
Use both hands to pull on any graspable features
Bring object toward center of the manipulable workspace
Bring toward mouth
If something doesn’t work at first…
Keep trying!
[1] Gray, L.A. et al., Evolution of Forelimb Forelimb Movement Patterns for Prey Manipulation in Anurans, J. Exp. Zoology, 277:417–424 (1997)
[2] Comer, C. and Grobstein, P., Tactually Elicited Prey Acquisition Behavior in the Frog, Rana pipiens, and Comparison with Visually Elicited Behavior J Comp Physiol (1981) 142:141-150
[3] Ivanco, T.L. et al., Skilled forelimb movements in prey catching and in reaching by rats and opossums, Behavioural Brain Research, 79 (1996) 163-181
[4] Rizzi, A. et al., Sequential Composition of Dynamically Dexterous Robot Behaviors, IJRR 1999; 18; 534.
Frogs grasping crickets (3 FPS) - A. Asbeck

## Slide 15: Grasping and sensing reflexes used to monitor normal infant development.
Twitchel, T.E, The Automatic grasping responses of infants,
Neuropsycholgia, Vol. 3, pp. 247-259 1965.

## Slide 16: Avoidance
Twitchel, T.E, The Automatic grasping responses of infants,
Neuropsycholgia, Vol. 3, pp. 247-259 1965.

## Slide 17: Other biological exemplars
Slit sense organs
Scorpion: 76 / leg
Spider: 224 / leg
Senses strains on the leg
Exoskeleton structures make the sensors possible (intrinsic tactile sensing)
Able to sense forces applied to areas elsewhere on the leg
Used in prey location - timing of spikes for 50m/s Rayleigh waves, ~300 Hz
Additional hair sensors give contact locations
[1] F. G. Barth and M. Wadepuhl. Slit Sense Organs on the Scorpion Leg. Journal of Morphology, 145 (2): 209-227, 1975
[2] F. G. Barth and J. Stagl. The Slit Sense Organs Arachids. Zoomorphologie, 86:1-23, 1976
[3] W. Sturzl, R. Kempter, J.L. van Hemmen, Theory of Arachnid Prey Localization, Physical Review Letters, v. 84, n. 4, June 2000.
10 mm
[2]
[1]

## Slide 18: Amoeba touch response
membrane
hyaline
layer
granular
cytoplasm
I. Joan Lorch, Cha 1, in The Biology of the Amoeba,
Kwang Jeon, ed., Academic Press, NY, 1973.